## Slide 1: Faculty of German Engineering and Industrial Management Education - FDIBA Introduction to Computer Graphics Drawing Lines
Assoc. Prof. Stoyan Maleshkov
Technical University of Sofia

## Slide 2: Line Drawing
Draw a line on a raster screen between two
points.
What’s wrong with the statement of the
problem?
  it doesn’t say anything about which points are allowed as endpoints
  it doesn’t give a clear meaning to “draw”
  it doesn’t say what constitutes a “line” in the raster world
  it doesn’t say how to measure the success of a proposed algorithm

## Slide 3: Line Drawing
Problem Statement
Given two points P and Q in the plane, both with integer coordinates, determine which pixels on a raster screen should be on in order to make a picture of a unit-width line segment starting at P and ending at Q.

## Slide 4: Basic Problem
Scan Conversion or rasterization
Due to the scanning nature of raster displays
Transforming the continuous into this discrete (sampling)
Algorithms are fundamental to both 2-D and 3-D computer graphics
Most of the early scan-conversion algorithms developed for plotters can be attributed to one man, Jack Bresenham

## Slide 5: Drawing Lines
For horizontal, vertical and diagonal lines all
pixels lie on the ideal line: special case
• For lines at arbitrary angle, pick pixels closest to the ideal line (Bresenham’s = midpoint “scan conversion” algorithm)

## Slide 6: Drawing Lines (2)
For thick lines, use multiple pixels in each column or fill a rotated rectangle

## Slide 7: Quest for the Ideal Line
The best we can do is a discrete approximation of an ideal line
Important line qualities:
  Continuous appearance
  Uniform thickness and brightness
  Turn on the pixels nearest the ideal line
  How fast is the line generated

## Slide 8: Simple Line
Based on the simple slope-intercept algorithm from algebra y = m x + b

## Slide 9: The Basic Algorithm:
Find the equation of the line that connects the two points P and Q.
Starting with the leftmost point P, increment xi by 1 to calculate y i = Ax i + B, where A = slope, B = y intercept.
Intensify the pixel at (x i , Round(y i )), where Round(y i ) = Floor(0.5 + y i )

## Slide 10: Simple Line Algorithm
public void lineSimple(int x0, int y0, int x1, int y1, Color color)
{ int pix = color.getRGB();
int dx = x1 - x0; int dy = y1 - y0; raster.setPixel(pix, x0, y0);
if (dx != 0) {
float m = (float) dy / (float) dx;
float b = y0 - m*x0;
dx = (x1 > x0) ? 1 : -1;
while (x0 != x1) {
x0 += dx;
y0 = Math.round(m*x0 + b);
raster.setPixel(pix, x0, y0); } } }

## Slide 11: Simple Line Algorithm
Demonstration

## Slide 12: Improved Line Algorithm
Problem:
lineSimple( ) does not give satisfactory results for slopes > 1

## Slide 13: Solution: symmetry
if (Math.abs(dx) > Math.abs(dy)) { // slope < 1
// Draw the line incrementing x0 …
}
} else if (dy != 0) { // slope >= 1
float m = (float) dx / (float) dy; // compute slope
float b = x0 - m*y0;
dy = (dy < 0) ? -1 : 1;
while (y0 != y1) {
y0 += dy;
raster.setPixel(pix, Math.round(m*y0 + b), y0); }

## Slide 14: Improved Line Algorithm
Demonstration

## Slide 15: Optimized Line Algorithm
Perform all calculations with integer variables
Rewrite the algorithm, that it use only addition
Result: Bresenham Algorithm

## Slide 16: Bresenham Algorithm

## Slide 17: Benchmarking
Demonstration

## Slide 18: Drawing Filled Polygons
1. Find intersection of scanline with polygon edges
2. Sort intersections by increasing x
3. Fill the polygon between pairs of
intersections (spans)

## Slide 19: Drawing Circles and Ellipses
Use symmetry

## Slide 20: Thickness Attribute
• Thick circle drawn by tracing a rectangular
pen