## Slide 1: Faculty of German Engineering and Industrial Management Education - FDIBA Introduction to Computer Graphics Graphics Devises
Assoc. Prof. Stoyan Maleshkov
Technical University of Sofia

## Slide 2: Graphics Devices
Principles and Constraints
Hardware
  Standard
  Graphics Devices
    Output
      Display
      Printer
      Plotter
    Input
      Various Types

## Slide 3: Standard Hardware
Typical Features
Moore’s Law
– price/performance improves 2x every 18 months due to doubling of number of transistors
– only exponential in technology except for growth of WWW
For more Information...
RAM: 256 - 512 MB, CPU: Pentium , AMD: 12000 – 3200 MHz
HDD: 20 -200 GB, Display: 1600/1200/true color

## Slide 4: Display Technologies
Cathode Ray Tubes (CRTs)
  Most common display device today
  Evacuated glass bottle (last remaining vacuum tube)
  Heating element (filament)
  Electrons attracted to focusing anode cylinder
  Vertical and Horizontal deflection plates
  Beam strikes phosphor coating on front of tube

## Slide 5: Display – Basic principle
Cathode Ray Tube (CRT)

## Slide 6: Display Technologies
What happens when the beam moves to another point of the display surface?

## Slide 7: Display Technologies
Display list had to be constantly updated (except for storage tubes)
  Storage Display
  Refresh Display

## Slide 8: Graphics Devices
2 Types of Displays:
  Vector
  Raster

## Slide 9: Vector Display
How the Image is generated

## Slide 10: Raster Display
How the Image is generated

## Slide 11: Vector Display
Architecture of Vector Display

## Slide 12: Raster Display
Architecture of Raster Display

## Slide 13: Raster Display
Frame buffer
Monochrome Display
  Frame Buffer М *N

## Slide 14: Raster Display
Architecture
For more Information...
DAC – Digital to Analog Converter – controls the intensity of the electron beam

## Slide 15: Raster Display
  Color CRTs are much more complicated
  Three electron guns
  Less bright than monochrome CRTs
  How do we represent Color in Graphics Systems ?

## Slide 16: Elements of Color

## Slide 17: Visible Spectrum
We perceive electromagnetic energy having wavelengths in the range 400-700 nm as visible light

## Slide 18: Raster Display
  How to describe Color – Color Models
  Additive Color Model: adding 3 primary colors
  Valid for emitting light sources Displays
  Primary Color
    Various possibilities
    Most popular - R G B

## Slide 19: Raster Display
  Color Model - R G B

## Slide 20: Raster Display
  Color Model - R G B

## Slide 21: Raster Display
  How does it work

## Slide 22: Raster Display
Delta Electron Gun Arrangement

## Slide 23: Raster Display
In-line Electron Gun Arrangement

## Slide 24: Raster Display
Disadvantages
  Requires screen-sized memory array
  Discrete spatial sampling (pixels)
  Moire patterns result when shadow-mask and dot-pitch frequencies are mismatched
  Convergence (varying angles of approach distance of e-beam across CRT face)
  Limit on practical size (< 40 inches)
  Spurious X-ray radiation
  Occupies a large volume

## Slide 25: Raster Display
Advantages
Allows solids to be displayed
Leverages low-cost CRT H/W (TVs)
Whole Screen is constantly updated
Bright light-emitting display technology

## Slide 26: Raster Display
  Color Display
  Frame Buffer – organized in Bit planes
  n Bit planes М * N Pixels
Pixel

## Slide 27: Raster Display
  Color Display– Video Lookup Table
  True color
    Each primary color is represented with 8 bits
    Total 3 colors * 8 Bits = 24 Bits/Pixel
Pixel

## Slide 28: Raster Display
  Represent the Color:
  Video Lookup Table: 3 Colors * 4 Bits = 12 Bits
  Frame buffer 8 Bit planes (n=8)
  28 = 256 Color Indices
Pixel

## Slide 29: Raster Display
    Represent the Color:
    Video Lookup Table: 3 Colors * 4 Bits = 12 Bits
    Frame buffer 8 Bit planes (n=8)
    28 = 256 Color Indices

## Slide 30: Raster Display
    Represent the Color:
    Video Lookup Table: 3 Colors * 4 Bits = 12 Bits
    Frame buffer 8 Bit planes (n=8)
    28 = 256 Color Indices

## Slide 31: Graphics Devices
Principles and Constraints
Hardware
  Standard
  Graphics Devices
    Output
      Display
      Printer
      Plotter
    Input
      Various Types

## Slide 32: Input Graphics Devices
Physical Devices
  Various Types
    Keyboard
    Mouse
    Trackball
    Joystick
    Data glove
    Digitizer
    Scanner – 2D, 3D
    Light Pen

## Slide 33: Input Graphics Devices
Physical Devices
  Trackball

## Slide 34: Input Graphics Devices
Physical Devices
  Z-Mouse

## Slide 35: Input Graphics Devices
Physical Devices
  Data Glove

## Slide 36: Input Graphics Devices
Physical Devices
    Digitizer

## Slide 37: Input Graphics Devices
Physical Devices
    Scanner – 3D

## Slide 38: Input Graphics Devices
Logical Devices
  Locator
  Selector
  Choice
  Text
  Valuator

## Slide 39: Input Graphics Devices
Logical Devices
  Logical Devices
  Locator, to indicate a position and/or
  orientation
  Pick (select), to select a displayed entity
  Valuator, to input a single value in the
  space of real numbers
  Keyboard, to input a character string
  Choice, to select from a set of possible
  actions or choices

## Slide 40: Input Graphics Devices
Implementation of Logical Devices
  Locator Devices: Tablet, Mouse, Trackball,
  Joystick, Touch Panel, Light Pen
  Keyboard devices: Alphanumeric keyboard
  (coded - get single ASCII character,
  unencoded - get state of all keys - more
  flexible)
  Valuator Devices: Rotary dials (Bounded or
  Unbounded), Linear sliders
  Choice Devices: Function keys

## Slide 41: Input Graphics Devices
Input Modes
  Request
  Sample
  Event

## Slide 42: Event Mode
  Generate initial display
  repeat
  Enable selection of commands and objects
  (Program pauses and waits until user acts)
  wait for user selection
  case on selection
  Process selection to process command
  Update model and screen as needed
  until quit ( User has selected the quit command)